# Error detection with CRC
Consider a message 110010 represented by the polynomial M(x) = x5 + x4 + x
Consider a generating polynomial G(x) = x3 + x2 + 1 (1101)
This is used to generate a 3 bit CRC = C(x) to be appended to M(x).
Note this G(x) is prime.
Steps:
1. Multiply M(x) by x3 (highest power in G(x)). i.e. Add 3 zeros. 110010000
2. Divide the result by G(x). The remainder = C(x).
   1101 long division into 110010000 (with subtraction mod 2)
   = 100100 remainder 100
  Special case: This won't work if bitstring = all zeros. We don't allow such an M(x).
  But M(x) bitstring = 1 will work, for example. Can divide 1101 into 1000.
  If: x div y gives remainder c
  that means: x = n y + c
  Hence (x-c) = n y
  (x-c) div y gives remainder 0
  Here (x-c) = (x+c)
  Hence (x+c) div y gives remainder 0
  110010000 + 100 should give remainder 0.
3. Transmit 110010000 + 100
   To be precise, transmit: T(x) = x3M(x) + C(x)
   = 110010100
4. Receiver end: Receive T(x). Divide by G(x), should have remainder 0.
Note if G(x) has order n - highest power is xn,
then G(x) will cover (n+1) bits
and the remainder will cover n bits.
i.e. Add n bits to message.
- Digital Communications course by Richard Tervo
  - Error detection with CRC
- Some CRC polynomials that are actually used
  - e.g. The 802.3 (Ethernet) polynomial adds 32 bits to the message.